Title
RTLinux in an FPGA
Alejandro Lucero
alucero@os3sl.com
www.os3sl.com

---
RTLinux in a FPGA
1. OpenRTU Project
2. FPGAs and soft processors
3. uClinux
4. RTLinux in Microblaze

---
1. OpenRTU Project
Spanish Industrial Research Project (Nov, 2004 – May, 2006)
Financed by Spanish Industrial Ministry (PROFIT)
Consortium:
TELVENT: real time company, RTUs
ESI: European Software Institute, Product Line
CSIC: Scientific Research Institution, FPGA Design
OS3: embedded Linux company, RTLinux

---
1. OpenRTU: Project Goal
Building a new generation of RTUs (Remote Terminal Units) using FPGAs and Open Source.
More Flexibility
Faster Development
Better Scalability
Avoiding Obsolescence Challenge

---
1. OpenRTU Project: Results
A prototype built and running uClinux
and RTLinux in Microblaze
HARD Real Time requirements
achieved (Initially, 1ms)

---
2. FPGAs and soft processors
FPGA: Field Programmable Gate Array
Device containing programmable logic and programmable interconnects.
Field programmable = it can be programmed after the manufacturing process in the field
You can program the HW !!!

---
2. FPGAs: How it can be programmed
FPGA design using VHDL (VHSIC & HDL)
An Electronic Automation Tool obtains a netlist from the VHDL code
Place & Route software fits the netlist to the FPGA
Validation through timing analysis, simulation and verification tools
A bitstream is generated to program the logic gate array

---
2. FPGAs: How it can be programmed
You can add IP (Intellectual Property) Cores to your design: libraries of predefined complex functions and circuits
IP Cores: buses, codecs, DSPs, interfaces, ... and processors
Soft processors (FPGA logic): picoblaze (Xilinx), Microblaze (Xilinx), Nios (Altera), LatticeMico32

---
2. FPGAs: Microblaze soft processor
Xilinx Microblaze (4.0) 32 bits processor
Three-stage pipeline
RISC, Harvard architecture
Configurable Code and Data Caches
Hardware Debug Logic
Non-MMU processor

---
3. uClinux
Linux for non MMU processors
Available ports: DragonBall, Coldfire, QUICC, ARM7DMI, Intel i960, Blackfin, Microblaze, NEC V850
Commercial products based on uClinux: IP cameras, wireless routers, VoIP based telephones

---
3. uClinux: drawbacks
No protection between tasks, and even worse: a user process can crash the system
This is the most well-known issue, but it is not the only one
Using Linux code is not automatic

---
3. uClinux: non MMU problems
Processes are created using the vfork system call instead fork
user stack per process is static in size
memory management done by the OS is different
dynamic libraries are not available (at least as standard)

---
3. uClinux: Microblaze Architecture
Port done in 2003 by John Williams, from Queensland University in Australia
uCLinux 2.4 in Microblaze is being used in several commercial products
Xilinx has recently released the uClinux 2.6 for Microblaze

---
4. RTLinux
RTLinux is a hard real time microkernel
Interrupts are virtualized for Linux
Linux runs as the task with the lowest priority inside RTLinux: Linux is the idle task for RTLinux

---
Virtualization technology is in fashion

---
RTLinux Virtualization technology

---
4. RTLinux in Microblaze
RTLinux DOES NOT need an MMU (but can use it)
RTLinux needs Linux or uClinux: uClinux port in Microblaze done by John Williams in 2003
What HARD real time performance can be achieved with a 75Mhz soft processor running a GPOS?

---
4. RTLinux in Microblaze: Doing the PORT
We had some initial doubts about the technology
These doubts were reinforced when we found a bug in the processor IP core implementation
This led us to put most of the blame on the technology when latencies were not as expected

---
4. RTLinux in Microblaze: Doing the PORT
We decided to divide the work clearly:
1) Interrupts virtualization layer
2) RTLinux microkernel
In case of problems with the full RTLinux microkernel coexisting with uClinux kernel, we could just make use of the virtualization mechanism for a simple system executing critical code when an event raises an interrupt without uClinux interference

---
4. RTLinux in Microblaze: Doing the PORT
Once the Interrupt Virtualization layer was implemented, first tests showed latencies higher than expected
The measurements were done with the timer interrupt, and Linux could be interfering with the results
We decided to wait until we knew what latencies we had with the full RTLinux microkernel working
... But we suspected OPB (On-Chip peripheral Bus) was introducing the delays

---
4. RTLinux in Microblaze: Doing the PORT
The second part of the work was done to implement the full RTLinux microkernel: threads creation and destruction, scheduling, timer programming (one shot and periodic) and threads synchronization and communication
The RTLinux microkernel code is composed of architecture specific part, and by independent architecture which will run without changes

---
4. RTLinux in Microblaze: Doing the PORT
Once the full RTLinux microkernel was implemented, tests showed peak latencies higher than expected
We did some code inspection but in C language level
Due to our initial doubts about the uncertainty of the technology, we suspected OPB was introducing the delays
This took us to the longest route to solve the problems, but on the positive side, this was not a complete waste of time.

---
4. RTLinux in Microblaze: Doing the PORT
The solution taken was to make use of a special Microblaze configuration avoiding the execution of real time code from DRAM or SRAM
LMB and Microblaze caches have 1 cycle access
The idea was to allocate the real time code into these special memories avoiding the peak latencies when the code had to go through the OPB

---
4. RTLinux in Microblaze: Doing the PORT
Drawbacks when using 1 cycle access memories
LMB Ram Blocks are used by FPGA designers, so we can not take them for free.
Microblaze cache is write-through, so if the problem is when RAM or SRAM is accessed, we are in the same point

---
4. RTLinux in Microblaze: Doing the PORT
The first problem was maximum space available (Spartan3) using LMB was 16Kbytes (just 12Kbytes aligned)
RTLinux modules:
rtl.o:	8192 bytes (only code)
rtl_time.o	2264 bytes (only code)
rtl_sched.o	13692 bytes (only code)

---
4. RTLinux in Microblaze: Doing the PORT
RTLinux code distribution was modified, creating a new module where "real" real time code is allocated
In the old modules we left the code just used during initialization
the new module rtl_previous_core had a final size of 8K, so it could be allocated in the LMB

---
4. RTLinux in Microblaze: Doing the PORT
We did other changes in uClinux related with interrupts code: a new section was created in the elf kernel file for this code, and during the initialization it is copied to LMB
Once we had all the code related with real time in 1 cycle memory access, we did new tests and ...
Peaks latencies had survived the attack

---
4. RTLinux in Microblaze: Doing the PORT
Technology was absolved. We had the real guilty:
The RTLinux Port Implementation was buggy

---
4. RTLinux in Microblaze: Doing the PORT
Some problems hard to find:
Microblaze has not lock instructions: changes in set_bit, test_bit, clear_bit, test_and_set, test_and_clear, which need to disable interrupts.
Some cli uClinux operations were not being virtualized
compilation flags: muls and divs by software introduce high latencies
buggy gcc 2.95 with 64 bits operations (needed for timers)

---
4. RTLinux in Microblaze: Results

---
4. RTLinux in Microblaze: Doing the PORT
Conclusions
we followed the longest route to achieve the hard real time performance
The usual way would had been to suspect first that the implementation is buggy, but we had some preconceived ideas...
On the positive side, we have now the best performance we can get using RTLinux and uClinux in Microblaze

---
Thank you
Alejandro Lucero
alucero@os3sl.com