Porting devices drivers to the 2.6 kernel
Craig Duffy
Bristol UWE
craig.duffy@uwe.ac.uk

---
Introduction and overview
We will look at a practical example of porting a device on a board onto 2.4 then to 2.6
We will then look at the ways that 2.6 has improved (or otherwise) the process of porting drivers
We will also look in a bit more detail at the underlying model that supports the new 2.6 model
We will also look at some of the new features – especially sysfs and how it can be used

---
The Puppeteer SA1110 board
SA1110 based board
Has SMSC91C96I NIC
ALTERA 6K FPGA
Toshiba AFE (codec)
Used in University embedded systems courses
Original designed for WinCE, then had VXWorks ported onto it, now uses Linux (2.6.20!)

---
The SMSC 91C96I NIC
The SMSC 91C9CI is part of the smc91xx series of Ethernet chips that are heavily used in embedded boards
The chip is similar in design and function to other Ethernet chips
We will briefly look at the chip and its features and then look at the driver support in the 2.4 series kernel (circa 2.4.18)

---
The SMC91C96I features
The SMSC91C96I features
Originally ISA bus based chip
  - supports PCMCIA, M68k and local bus version
Half and full duplex chip
Has 6k bytes of on board ram memory
  - controlled by an on-chip MMU
Supports IEEE 802.3 (Ethernet)
Status leds
Has magic packet!

---
The SMSC91C96I Register Set
There are a series of banks of control and status registers, one of which is available through a memory address.
Bank 1 is generally set up via EEPROM data at boot time
  - this is not always true!
Bank 2 is the default visible bank during run-time
The others are generally used during initialisation or reset

---
The SMSC registers
BANK 0
BANK 1
BANK 2
BANK 3
BANK 4
TCR
EPH
Status
RCR
Multicast
Counter
MIR
MCR
General
Purpose
Reserved
Control
Table
MGMT
Revision
ERCV
ECOR low
ECSR high
Bank Select Register
MMU
Command
PNR
ARR
FIFO
Ports
Pointer
Data
Data
Interrupt
Config
Base
Individual
Address0-1
2-3
4-5
Bank 2 Registers used at run time
Stored in EEPROM

---
Linux SMC9194 device driver
Linux SMC9194 device driver
Doesn’t work out of the box! (with rmk7 patch applied)
  - There are a few lines that need editing before it will compile
It requires quite a bit of configuration for our system
  - The memory address of the chip on our board needs specifying
  - Our system uses an FPGA to do some of the SA1110's interrupt handling and the FPGA set up and IRQ code needs writing and incorporating into the driver

---
The SMC9194 driver
There are a number of different routines – for example
  - Initialisation routines
    - smc_init, smc_probe, smc_probe_irq
  - Interface routines
    - smc_open, smc_close
  - Internal routines
    - smc_wait_to_send_packet, smc_hardware_send_packet
  - lots of macros + stats gathering functions
  - lots of interrupt handling routines

---
SMC9194 Initialisation
The smc_init function gets included, via register_netdev, into the list of initcalls in <linux/init/main.c>
  - If used as a module smc_init is called directly
This function then calls probe functions which check to see if there is an smc chip
  - smc_probe, smc_probe_chip
Interrupts are (optionally) probed and initialised
You get a nice friendly message in dmesg!

---
smc_init code
#ifdef (CONFIG_SA1100_PUPPETEER)
dev->base_addr=0xf3800300;
dev->irq=1;
base_addr = dev->base_addr;
SET_MODULE_OWNER(dev);
set_GPIO_IRQ_edge(GPIO_GPIO1, GPIO_RISING_EDGE);
fpga_addr = ioremap(0x10400000, 0x700);
if (!fpga_addr)
  {
    printk("Can't get memory for FPGA\n");
    return -ENOMEM;
  }
reg = readw(fpga_addr + (0x104/2));
reg &= ~0x20;
writew(reg , fpga_addr + (0x104/2)); //polarity reg set bit 5 to 0
reg = readw(fpga_addr + (0x104/2));
reg = readw(fpga_addr + (0x106/2));
reg &= ~0x20;
writew(reg , fpga_addr + (0x106/2)); //edge reg set bit 5 to 0
reg = readw(fpga_addr + (0x106/2));
reg = readw(fpga_addr + (0x102/2));
reg |= 0x20;
writew(reg , fpga_addr + (0x102/2)); //enable reg 1 bit 5
reg = readw(fpga_addr + (0x102/2));
reg = readw(fpga_addr + (0x100/2));
reg |= 0x20;
writew(reg , fpga_addr + (0x100/2)); //status reg 1 bit 5
reg = readw(fpga_addr + (0x100/2));

---
SMC_INIT CODE cont.
/* try a specific location */
addr = ioremap(0xf3800300, 10 * 16);
if (!addr)
  return -ENOMEM;
ret=smc_probe(dev, base_addr);
iounmap(addr);
/*clear interrupt from the test on the fpga */
reg = readw(fpga_addr + (0x100/2));
reg |= 0x20;
writew(reg , fpga_addr + (0x100/2)); //status reg 1 bit 5
reg = readw(fpga_addr + (0x100/2));
GEDR |= GPIO_GPIO1;
iounmap(fpga_addr);
#endif

---
2.4 review
Requires some changes to the driver code
  - some (more?) is put into arch/arm/mach-sa1100/puppeteer.c
  - for the irqs it is hard to see how this could change
Driver could quite often hang up
  - this seems to be a problem of the internal MMU and not the driver code – it can be reset
The whole driver was rewritten and cleaned up and available as a patch and then included in the 2.6 release
  - smc91x.c/h

---
The 2.6 smc91x driver
The new smc91x driver has been substantially rewritten during the 2.6 series life allowing it to integrate it into the new device model
All of the data for device initialisation is declared in the arch/arm/mach_xx/machine.c file
The device registration with the new model is achieved with the platform_add_devices call, called from the above file

---
puppeteer.c
........
#include <linux/platform_device.h>
........
#include "generic.h"
/* Ethernet IRQ mappings*/
#define PUP_ETH0_P	(0x20000300)
#define PUP_ETH0_V	(0xf3800300)
#define GPIO_ETH0_IRQ	GPIO_GPIO(1)
#define IRQ_GPIO_ETH0_IRQ	IRQ_GPIO1
static struct resource smc91x_resources[] = {
[0] = {
.start	= PUP_ETH0_P,
.end	= PUP_ETH0_P | 0x03ffffff,
.flags	= IORESOURCE_MEM,
},
[1] = {
.start	= IRQ_GPIO_ETH0_IRQ,
.end	= IRQ_GPIO_ETH0_IRQ,
.flags	= IORESOURCE_IRQ,
},
};
static struct platform_device smc91x_device = {
.name	= "smc91x",
.id	= 0,
.num_resources	= ARRAY_SIZE(smc91x_resources),
.resource	= smc91x_resources,
};
static struct platform_device *devices[] __initdata = {
&smc91x_device,
};
.......
static void __init puppeteer_init(void)
{
  int status;
  platform_add_devices(devices, ARRAY_SIZE(devices));
  sa11x0_set_mcp_data(&puppeteer_mcp_data);
}

---
smc91x initialisation
As more initialisation data is placed in the arch/arm/mach-xx/machine.c file there is less requirement to change drivers/net/smc91x.c
However, the FPGA/IRQ code still needs addressing
  - this has to be in the smc91x driver
The initialisation is set up through the register_platform_device call
  - this is either called directly through an insmod call or through the device system initialisation
    - drivers/base/init.c -> drivers/base/platform.c (platform_driver_probe)

---
smc91x init code
static struct platform_driver smc_driver = {
.probe	= smc_drv_probe,
.remove	= smc_drv_remove,
.suspend	= smc_drv_suspend,
.resume	= smc_drv_resume,
.driver	= {
.name	= CARDNAME,
},
};
static int __init smc_init(void)
{
#ifdef MODULE
#ifdef CONFIG_ISA
if (io == -1)
printk(KERN_WARNING "%s: You shouldn't use auto-probing with insmod!\n",CARDNAME);
#endif
#endif
return platform_driver_register(&smc_driver);
}

---
smc91xc smc_drv_probe (nee smc_init)
/*
 * smc_init(void)
 * Input parameters:
 *	dev->base_addr == 0, try to find all possible locations
 *	dev->base_addr > 0x1ff, this is the address to check
 *	dev->base_addr == <anything else>, return failure code
 *
 * Output:
 *	0 --> there is a device
 *	anything else, error
 */
static int smc_drv_probe(struct platform_device *pdev)
{
struct net_device *ndev;
struct resource *res;
unsigned int __iomem *addr;
int ret;
unsigned short * fpga_addr, reg; /* Craig Duffy 9/2/7/*/
res = platform_get_resource_byname(pdev, IORESOURCE_MEM, "smc91x-regs");
if (!res)
res = platform_get_resource(pdev, IORESOURCE_MEM, 0);
if (!res) {
ret = -ENODEV;
goto out;
}
............
............

---
The 2.6 device model
As we have seen that the driver now interfaces into the a part of the new driver model
  - into the platform bus
We now need to look in a bit more detail at the this model
To do this we need to know about kobjects, ktypes, ksets and subsystems
  - this model is closely tied to sysfs, udev and hotplug

---
Kobjects
The kobject can be viewed rather like an OOP abstract class Object
It is deeply embedded in the device model
Its description can be found in <linux/kobject.h>

---
kobjects
kobjects don't do very much on their own!
They have a reference count
They have names
They are stored in linked lists of object hierarchies
They are embedded in other structures and allow them to be linked into an object hierarchy

---
ktypes
ktypes are associated with kobjects
They give a description of the kobject's behaviour and attributes
Their definition can be found in <linux/kobject.h>

---
ksets
ksets are aggregates of kobjects – rather like a base container class
Collections of similar objects can be held in a kset – all block devices for example
It is defined in <linux/kobject.h>

---
Subsystems
Subsystems are loose aggregations of ksets
Unlike ksets the susystem ksets and kobjects may only have a transitory/arbitrary relationship
defined in <linux/kobject.h>

---
Linking it together
If we look at our smc network device driver we can see that
  - it is of kobject type platform_device
  - it belongs to the kset platform_bus
  - and platform_driver belongs to the subsystem bus
also, through sysfs we can see that the smc device driver is in the subsystem devices

---
sysfs
From the previous we can see how sysfs can be used with the device model to allow information about device, drivers and buses to be easily accessible
It is possible to create new macros to output device/driver/bus information
  - such as the device name or major number
    - this can be used by udev – see udevinfo -p

---
sysfs output

---
2.6 device driver model?
For
  - bus based
    - reduces duplication
    - allows greater hierarchical control over peripherals
      - i.e. power control
  - Less change to device code
  - Cleaner API
Against
  - Have to learn complex model
  - Too greater integration of sub-systems
    - bad for embedded?
  - Hides implementation details
    - bad for embedded?

---
In conclusion
It needs to be recognised that the device model is not making Linux into an object orientated OS
  - we need to be careful with terminology
For embedded systems the high level of integration between the model, sysfs, udev and hotplug may not be good
sysfs can be confusing but procfs was being seriously over extended
With real buses (i.e. not platform) large efficiency savings can be made

---
Finally (at last!)