Running Valgrind
on multiple processors:
a prototype
Philippe Waroquiers
FOSDEM 2015 valgrind devroom

---
Valgrind and threads
- Valgrind runs properly multi-threaded applications
- But (mostly) runs them using a single CORE
- Valgrind needs a lot of CPU :
  - Depending on the tool,
    single-threaded applications
    are slowed down
    by a factor 4x to 100x or more

---
Valgrind and CPU consumption
- Significant development effort was and is spent to make Valgrind faster e.g.
  - Improvement of the JIT generated code
  - Self-modifying code detection
  - Translation chaining
  - Tool specific performance improvement
  - …

---
Improving Valgrind speed
- Improving 'sequential' speed is good for all applications
  - However, often, the last years, the gains are small
    typically around 5 .. 10%
- Multi-threaded CPU bounded applications
  would benefit a lot from parallelising Valgrind
  - But how hard is that ?

---
Valgrind layers
Tool “runtime” code
Tool instrument function
TOOL
Generated/instrumented code
(from program to run)
GUEST
JIT decoder and compiler, malloc replacement, scheduler, ...
Valgrind CORE
layer

---
Valgrind layers typical control flow
1. CORE decodes guest code : instructions to IR
2. CORE calls TOOL instrument : IR to IR.
   Instrumented code typically contains many calls to TOOL runtime code or CORE code.
3. CORE translates instrumented code to executable code : IR to instructions
4. Instructions stored in the translation table
5. Valgrind scheduler calls the translation

---
(Most of) Valgrind code is
non-reentrant/non thread-safe
- Translation is non thread-safe: VEX lib, tool instrument function, CORE translation framework, ...
- “Run time” is non thread-safe:
  - CORE scheduler, CORE malloc/free, CORE aspacemgr, CORE statistics, …
  - TOOL runtime code, e.g. memcheck malloc/free, memcheck VA bits data structures, …
- So, why is Valgrind able to run properly multi-threaded applications ?

---
Valgrind “big lock” model
- Valgrind has a big lock
  - The big lock protects all Valgrind data structures/all Valgrind global variables/all tool data structures/...
  - Big lock implemented via a 'pipe based lock' (default) or via futex ('ticket lock'), cfr --fair-sched
- To execute JIT-ted guest or tool or core code,
  a thread first must acquire the big lock
- A thread releases the lock
  - After it has executed 100K basic blocks
   or
  - Before entering in a blocking syscall

---
To parallelise Valgrind
- We must
  - Remove the big lock
  or
  - At least decrease the use of the big lock

---
Parallelising Valgrind
possible techniques
- Read/write locks
- (fine grained) mutex locks
- Atomic instructions
- Thread local storage instead of global variables
- Lock-less algorithms/data structures
- ….
- A prototype has used some of the above to parallelise some (small) parts of Valgrind

---
What to parallelise (first) ?
- A typical tool/application spends most of CPU in the generated JIT code, in the TOOL and CORE “runtime” code
- The time spent in TOOL instrument function is normally not a major part
- => First idea: ensure that the threads are running guest JIT-ted code in parallel

---
Running JIT-ted code in parallel
Basic idea
- Replace 'mutex Big lock' by 'read/write Big lock'
- A thread acquires the RW Big lock
  - In read mode to run guest JIT-ted code
  - In write mode to do anything else
- First implementation of basic idea:
  - Objective: ensure 'none' tool runs in parallel
  - How : RW lock implemented on top of 'pipe based locks'

---
Running JIT-ted code in parallel
First implementation expected results
- Of course, first implementation will be efficient
  - As the pipe based lock is efficient enough for current Valgrind, the rw lock will be efficient enough for parallel use
- Of course, first implementation will be correct
  - As “none” tool means no Valgrind data structure are accessed when running JIT-ted guest code
- Of course, all above
  - was shown WRONG !!!

---
Running JIT-ted code in parallel
First implementation problems
- Lack of efficiency when translating new code:
  - When new code to be translated, sequential valgrind just keeps the lock
  - Parallel Valgrind needs to (re-)acquire the lock in Write mode => a lot more (expensive) 'lock/unlock'
- Lack of correctness
  - What looks like a 'read-only' action (execute already translated code) is in fact doing many updates e.g.
    - statistical counters
    - fast cache associating guest code with JIT code
    - Translation chaining
    - ...

---
Running JIT-ted code in parallel
Fixing first implementation
- Better way to find non thread safe code
  - Valgrind and helgrind were improved to allow to run an 'inner parallel valgrind' under an outer helgrind
  - Improvements are now in Valgrind release :
    it is now easy/ier to run Valgrind under Valgrind
  - Helgrind was used to find race conditions in prototype parallel Valgrind
- Efficiency :
  - RW lock based on (slow) pipe based mutexes replaced by RW lock code copied/modified from glibc

---
Read the patch...
Prototype code accessible in SVN MTV branch
see also doc/internals/mtV.txt

---
Multi-threaded Valgrind : challenges
Valgrind core
- Make (more of) core parallel/thread-safe
  - Prototype is far to be complete/correct
- Probably/maybe we need an option
  to have sequential run of parallel tools
  (e.g. to avoid memcheck false + or -)
  or avoid running non parallel tools in parallel
- Implement atomic ops for other arch
- What about Darwin and fast mutex ?

---
Multi-threaded Valgrind : challenges
Making Valgrind tools parallel
- At least memcheck (the most used tool)
- Keep cpu and/or memory efficiency is difficult
  (apart of trivial tools such as --tool=none)
- No tool was made parallel (except none)
  - Parallel memcheck somewhat discussed/tried
  - Draft proposal of new VA-bits approach made by Julian Seward

---
Multi-threaded Valgrind : challenges
Memcheck VA-bits data structure
- Is currently highly optimised, CPU and memory
- No solution found that at the same time
  - Is efficient in CPU and memory
  - and has no false + and/or false -
- Maybe make 'VA-bits read' inline fast, 'VA-bits write' use mutex ? (or an option to activate write mutex)
- Maybe we need tuning options such as
  --va-bits=sequential | parallel-cpu
  | parallel-memory | …

---
Multi-threaded Valgrind : challenges
- Probably many challenges not known yet …
  - Because not exercised by the prototype 'testing'
  - Many core modules not looked at
    e.g. Valgrind malloc, error mgr, stack unwind, ...
- Do all the above without slowing down the sequential case
  - Many optimisations to be redone/reworked !

---
Questions?