## Slide 1: An opensource SPDM implementation for secure device communication
Jiewen Yao, Principal Engineer, Intel
Xiaoyu Ruan, Principal Engineer, Intel

## Slide 2: Jiewen Yao
Jiewen Yao is a principal engineer in the Intel Architecture, Graphics, and Software Group. He has been engaged as a firmware developer for over 15 years. He is a member of the UEFI Security sub team, and the TCG PC Client sub working group.
He is the creator of the open source SPDMcode project.

## Slide 3: Xiauyu Ruan
Xiaoyu Ruan is a principal engineer in the Security Architecture and Engineering group at Intel. He has 17 years of experience in cryptography and security architecture and implementation on embedded systems.
He is a co-author of DMTF SPDM specifications.

## Slide 4: Part I - SPDM

## Slide 5: SPDM
DSP0274 Secure Protocol and Data Model Specification
Part of Distributed Management Task Force (DMTF) Platform Management Components Intercommunication (PMCI)
SPDM1.0 (Dec 2019) – Device authentication and measurement
SPDM1.1 (July 2020) – Device session key establishment and secure communication (session)
SPDM1.2 (WIP, ETA Q2 2021) – See later slide for candidate features
Adoption: DMTF, PCI/CXL, MIPI, USB, TCG, …

## Slide 6: SPDM 1.0
Device Measurement Collection / Attestation
Device Authentication
Device Identification
* source: SPDM 1.0 specification

## Slide 7: SPDM 1.1
Diffie-Hellman (DH) based Key Exchange +
(Mutual) Authentication
Pre-Shared Key (PSK) based Key Exchange
or
* source: SPDM 1.1 specification

## Slide 8: SPDM 1.2 Candidate Features
* source: OCP tech week 2020
Feature | Description
Set Certificate | A set of commands to manage certificate chains in slots 1-7. Could include CSR export and slot policies.
Eventing | Mechanism to send asynchronous events, related to SPDM, to a registered listener.
Multi-tier Authentication | A set of commands to authenticate devices behind non-transparent bridges. Under discussion, does the PA-RoT or intermediate device perform the authentication?
Smaller Certificates | Address the size issue with the current certificate / cert chain.
Measurement Manifests | Define a mechanism to produce a manifest of expected measurements for a given device, and modifications to the MEASUREMENTS command to report measurements in a way that is compatible with the reference manifest.
TCG DICE Support | Support the use of TCG DICE throughout SPDM, including in signature generation, Set Certificate, and events.
Reprovisioning | Mechanism to cause a device to generate a new set of Device Keys and invalidate all elements that depend on the existing Device Keys.

## Slide 9: Transport Layer Binding
SPDM Message
DMTF
SPDM over MCTP
DMTF
MCTP over SMBus
PCI
Data Object Exchange (DOE)
USB
Control Transfer
SMBus Device
PCI Device
USB Device

## Slide 10: TCG SPDM support
Described in TCG PC Client Platform Firmware Profile Specification (Draft public review)
Device measurement (hardware/firmware) –> TPM
  PCR2 (EV_EFI_SPDM_FIRMWARE_BLOB)
Device measurement (hardware/firmware configuration) -> TPM
  PCR3 (EV_EFI_SPDM_FIRMWARE_CONFIG)

## Slide 11: Part II - SPDMcode

## Slide 12: SPDMcode
An open-source SPDM sample implementation (requester or responder).
It is BSD licence.
It is written in C language.
It includes a fake SPDM requester and responder in OS.
It can dump/trace the SPDM message flow.

## Slide 13: SPDMcode design
SPDM Responder
Device
SPDM Requester
Device
SpdmRequesterLib
SpdmCommonLib
SpdmResponderLib
SpdmSecured MessageLib
SpdmTransportXXXLib
SPDMcode
SpdmDeviceIo
DSP0274 SPDM
DSP0277 Secured Message
DSP0275 SPDM Over MCTP
PCI DOE Message
DSP0237 MCTP Over SMBus
PCI DOE mailbox
Security Policy
Crypto Engine (Key, RNG, …)
Device RoT
Measurement
Crypto Engine
Crypto Engine
SpdmDevice SecreteLib
SpdmDevice SecreteLib

## Slide 14: Feature
Implemented SPDM 1.0 and 1.1.
Support openssl/embedtls/3rdPartyCryptoLib as crypto engine
Support algos defined in SPDM. (SHA/SHA3, RSASSA/RSAPSS/ECDSA, FFDHE/ECDHE, AES-GCM/CHACHA20-POLY1305)
Programming Context :No heap, no global variable.
Execution Context: Link as OS Application, UEFI Driver, BMC module, etc.
Build in Windows (VS2019/Clang), Linux (GCC/Clang).

## Slide 15: Additional work for SPDMcode consumer
Link a crypto library (maybe hardware accelerator)
Protect the private key
Provision the public certificate
Support random number seed and random number generator
Put SPDMcode in a protected execution environment
  to prevent local attack or side channel attack, etc.
Provide transport layer send/receive function.
Implement proxy to handle device measurement
  e.g. extend to TPM PCR or attestation
Support the different use case for SPDM secure session
  e.g. PCI express key programming, link encryption setup.

## Slide 16: Size
VS2019 (DLL) | Requester (K) | Responder (K)
Raw library, no crypto (X64) | 26 | 29
With mbedtls (X64) | 138 | 141
Raw library, no crypto (IA32) | 20 | 21
With mbedtls (IA32) | 110 | 111

## Slide 17: Demo (init connection)

## Slide 18: Demo (challeng/auth)

## Slide 19: Demo (session creation)

## Slide 20: Demo (secured message)

## Slide 21: SpdmDump tool
Similar to ssldump.
Assuming there is PCAP file available for all SPDM transation
  Sample provided by SPDM responder emu or SPDM requester emu.
Parse PCAP file and dump all SPDM transation in OS.
Support different mode (default, quite, all)
Support different transport layer
  MCTP or PCI_DOE
Support known SPDM vendor defined message dump.
  IDE_KM
Support secured message dump
  Need user input --psk or --dhe_secret.

## Slide 22: SpdmDump – SPDM over MCTP

## Slide 23: SpdmDump – SPDM over PCI_DOE

## Slide 24: SpdmDump – Secured SPDM

## Slide 25: SpdmDump – dump all mode

## Slide 26: Summary
SPDM specification
  It is well adopted in multiple standard orgnizations.
  SPDM can be used to authenticate device and collect measurement.
  SPDM session can be used for secure communication between devices.
SPDMcode
  It is an open source SPDM sample implementation.
  It is BSD license and written in C.
  It helps you learn SPDM and create SPDM capable devices.
  SpdmDump tool can help you analyse SPDM transaction.

## Slide 27: Reference
SPDM Specification
  DSP0274 - Security Protocol and Data Model (SPDM) Specification
  DSP0275 - Security Protocol & Data Model (SPDM) over MCTP Binding Specification
  DSP0276 - Secured MCTP Messages over MCTP Binding Specification
  DSP0277 - Secured Messages using SPDM Specification
  DSP2058 - Security Protocol and Data Model (SPDM) Architecture White Paper
  https://www.dmtf.org/standards/pmci
TCG SPDM Support
  TCG PC Client Platform Firmware Profile Specification (Draft for review)
  https://trustedcomputinggroup.org/wp-content/uploads/TCG_PCClient_PFP_r1p05_v22_02dec2020.pdf
PCI Support
  ECR PCI Component Measurement and Authentication (CMA)
  ECR PCI Data Object Exchange (DOE)
  ECR PCI Integrity and Data Encryption (IDE)
  https://pcisig.com/specifications/review-zone
USB Support
  USB Authentication Specification
  https://www.usb.org/document-library/usb-authentication-specification-rev-10-ecn-and-errata-through-january-7-2019

## Slide 28: Reference
SPDMcode pre-production code / document
  https://github.com/jyao1/openspdm
  SpdmDump tool: https://github.com/jyao1/openspdm/tree/master/Tool/SpdmDump
EDKII pre-production code for device security
  https://github.com/jyao1/edk2/tree/DeviceSecurity

## Slide 29: Question