## Slide 1: Extending AF_XDP for fast co-located packet transfer
Debojeet Das, Kevin Prafull Baua, Aditya Kansara, Arghyadip Chakraborty, Dheeraj Kurukunda, Mythili Vutukuru, and Purushottam Kulkarni debojeetdas@cse.iitb.ac.in Systems and Networking Research Group (SynerG) Department of Computer Science and Engineering Indian Institute of Technology Bombay
FOSDEM’26 JAN 31, 2026

## Slide 2: Fast network I/O with XDP and AF_XDP
eBPF/XDP
In-kernel packet processing
- eBPF based
- eBPF restricted constraints
if (pkt.ip == a.b.x.x)
DROP
XDP and AF_XDP allows us to deploy our-own high-performance load balancer, firewall, etc.

## Slide 3: Fast network I/O with XDP and AF_XDP
eBPF/XDP
In-kernel packet processing
- eBPF based
- eBPF restricted constraints
if (pkt.ip == a.b.x.x)
DROP
AF_XDP
Partial kernel bypass via XDP - zero-copy delivery to user apps
- Interrupt driven/Busy poll
if (pkt.ip == a.b.x.x)
Redirect to AF_XDP sock 1
XDP and AF_XDP allows us to deploy our-own high-performance load balancer, firewall, etc.

## Slide 4: Co-locating multiple AF_XDP zero-copy apps
Goal: Efficient co-location of AF_XDP zero-copy apps to provide complex services Problem: AF_XDP lacks socket-to-socket redirection much less zero-copy transfers
X
NIC
Firewall
Load Balancer
Router

## Slide 5: Existing solutions for co-located packet transfers between AF_XDP sockets
Pros: No API modifications needed Cons: Limited AF_XDP support - VF support only in mlx5 - SF support only in ice and mlx5 Performance hit from app-to-app copying
SR-IOV

## Slide 6: Existing solutions for co-located packet transfers between AF_XDP sockets
Pros: No API modifications needed Cons: Limited AF_XDP support - VF support only in mlx5 - SF support only in ice and mlx5 Performance hit from app-to-app copying
*Possible Solution
Motivated from existing DPDK solutions like OpenNetVM, etc. Pros: Zero-copy packet transfers Cons: Requires new APIs Creates tight coupling between Apps and libraries
SR-IOV Userspace Chaining*

## Slide 7: Our work: In-kernel packet transfers for AF_XDP
Flexible co-location via AF_XDP kernel extensions
Zero-copy for shared memory sockets; single-copy for others
Backward compatible solution: Transparent redirection with zero changes to userspace APIs
FLASH: Fast Linked AF_XDP Sockets for High-Performance Chaining

## Slide 8: Split data path of AF_XDP
Driver handles RX/TX
UMEM (buffer pool) shared between userspace application and kernel
SPSC rings to maintain packet accesses
Fill Ring and Rx Ring used in packet reception
Tx Ring and Completion Ring used in packet transmission

## Slide 9: Packet Reception in AF_XDP
Applications provide free descriptors for DMA
Kernel allocates them to NIC
NIC DMA’s the packet to UMEM
napi_poll executes the XDP program which returns the socket where the packet should be sent
The Driver calls AF_XDP subsystem’s function to place the descriptor in Rx ring
Application reads 7. processes and 8. recycles descriptors.

## Slide 10: Packet transmission and modes of AF_XDP
8b. to 12. shows the transmission path which uses the Tx and completion rings
The kernel space operations are initiated by the driver with the help of AF_XDP subsystem functions*
Driver can either invoke them based on interrupts or via hints using sendto() and recvfrom() syscalls (Busypoll)
*The functions can be found at include/net/xdp_sock_drv.h

## Slide 11: Challenge #1 Ring semantics
Redirection violates SPSC (Single-Producer/Single-Consumer) semantics
Key Idea #1: Backward-compatible MP/MC lockless rings
CAS operations serialize MP/MC while maintaining SP/SC for userspace
struct xdp_ring {
u32 producer; // Old field; represents producer_tail
u32 consumer; // Old field; represents consumer_tail
u32 flags;
u32 producer_head; // Used only for MPSC
u32 consumer_head; // Used only for SPMC
};
int xskq_enqueue_desc(struct xsk_queue *q, u64 addr, u32 len, u32 flags);
bool xskq_dequeue_desc(struct xsk_queue *q, struct xdp_desc* desc, struct xsk_buff_pool *pool);

## Slide 12: Zero-copy redirection with MP / MC rings
Packet data stays in shared UMEM
FLASH can move packet descriptor from TX ring of App 1 to RX ring of App 2
FLASH brings back empty descriptor from fill ring of App 2 to completion ring of App 1
Fill ring becomes MC in kernel and Rx ring becomes MC in kernel
single-copy redirection works similarily but using memcpy

## Slide 13: Challenge #2: Batched redirections
We, batch redirections to amortize CAS overhead
u32 xskq_bulk_enqueue_descs(struct xsk_queue *q, struct xdp_desc* descs, u32 n_descs);
With new MPSC/SPMC rings, available capacity changes mid-redirection
FR descriptors cannot be returned without violating ring semantics
Key Idea #2: Partial TX + Descriptor Buffering
Order ring updates so any packet placed in TX is guaranteed to redirect
Buffer extra FR descriptors for use in the next iteration

## Slide 14: Challenge #3: Scheduling threads
To balance CPU utilization and performance a hybrid polling workflow is usually employed in applications:
Start in interrupt mode: Use poll() with the POLLIN flag to block until packets arrive
Switch to busy-polling: At high rates, switch to a busy loop using recvfrom() to continuously process packets
Revert to interrupt mode: When load decreases, return to interrupt mode
By default, hybrid polling across packet transfers doesn’t work
Moreover, during congestion, the sender must retry transmissions until space becomes available this leads to wastage of CPU cycles

## Slide 15: Smart polling and early backpressure detection
Key Idea #3: Smart Polling & Early Backpressure
Extends hybrid polling across redirection paths
Congestion Handling: Senders block via poll() (POLLOUT) until space
Wake-up Signal: Receivers use recvfrom() (MSG_MORE) to signal senders

## Slide 16: Challenge #4: Performance vs. safety
How to isolate zero-copy Apps from each other in multi-tenant settings?
Key Idea #4: FLASH monitor and safe runtime
FLASH Monitor: Offloads privileged tasks and manages access control
Rust Runtime: Ensures memory and packet isolation in multi-tenant setups

## Slide 17: But how do you specify the path of transfers?
We need a way to inspect active AF_XDP sockets and configure transfer rules between sockets
FLASH should then use the rules to access the rings and perform the transfers
But, the sockets (struct xdp_sock) and its rings are backed by process local fds
How do XDP get access of rings then?
It stores the struct xdp_sock in a map and uses XDP program to select the socket on packet reception
Our Solution: Expose a sysfs interface under /sys/kernel/flash to store the sockets and configure redirection rules*
For example, if there are two sockets and we want all packets from socket 1 to go to socket 2 # echo 2 | sudo tee /sys/kernel/flash/1/next
*We also support dynamic packet transfers

## Slide 18: How much change is needed to support all this?
~700 LoC in AF_XDP subsystem
The changes mostly augments new features to the AF_XDP subsystem
Requires straightforward patching in driver to ignore packet transmissions
bool xmit_batch(struct xsk_buff_pool *pool, unsigned int budget)
{
struct xdp_desc *descs = pool->tx_descs;
unsigned int nb_pkts = 0;
// Fetch a batch of descriptors for transmission
nb_pkts = xsk_tx_peek_release_desc_batch(pool, budget);
if (!nb_pkts)
return true;
// If redirection is configured, skip NIC transmission
if (pool->no_tx_out) // New lines
return nb_pkts < budget; // New lines
// Proceed with normal transmission
return nb_pkts < budget;
}
We have already added support for ixgbe, i40e, ice and mlx5

## Slide 19: FLASH performance gains
Baselines:
AF_XDP-SRIOV: AF_XDP over SR-IOV
OpenNetVM: DPDK userspace chaining Our work:
FLASH-ZC: FLASH C library zero-copy
FLASH-ZR: FLASH Rust library zero-copy
FLASH provides lowest latency among all solutions.
FLASH-ZC provides 1.1 x - 2.5 x higher throughput than SR-IOV
24-core Intel Xeon Gold 5418Y, 128 GB RAM, HT disabled - Mellanox Connect X-4 MT27700 40Gbps (mlx5) Ubuntu 22.04 LTS, Linux Kernel 6.10.6 – Chains of L2FWD switches – Used Pktgen for load generation

## Slide 20: Summary
The Problem: AF_XDP lacks native support for zero-copy packet redirection between co-located sockets
The Solution: FLASH extends the AF_XDP kernel subsystem to enable high-performance, transparent chaining
Key Ideas:
  MP/MC Lockless Rings
  Batching & Buffering
  Smart Polling
A sysfs interface for setting up the redirections

## Slide 21: Future Directions
From sysfs to XDP_EGRESS: Replace current sysfs-based rule configuration with a native XDP hook at the egress point
  packet-steering logic can be entirely programmable via eBPF
  Interesting use case of XDP_EGRESS? (LPC 2025)
Generalizing the service chaining framework to support diverse set of applications
mTCP Integration: Currently developing zero-copy support for TCP-based applications
Using SPMC/MPSC rings of AF_XDP for other use-cases:
  Packet redirection from one queue to another queue during ingress
We are also working on a Rust rewrite of FLASH monitor

## Slide 22
Thank You
debojeetdas@cse.iitb.ac.in
Project Link: